## Slide 1
Enabling a Resilient Power Sector through Constructive Regulation
OCCUR Annual Conference
Kurt G. Strunk Vice President, CRA
29 April 2026

## Slide 2: Framing the Role of Regulation in Grid Resilience
Regulatory structures
  Why it matters
  Resilience is becoming a more explicit objective in utility regulation as power systems face growing disruption risks from wars, pandemics, extreme weather, aging infrastructure, and changing resource and demand patterns.
  Regulators play a key role in overseeing and directing how utilities plan, invest, operate, and recover their costs.
1
2
4
3
How industry structure affects the role of regulation in delivering resilience
Regulatory tools used to support resilience, from standards and planning to cost recovery and performance oversight
How different jurisdictions approach resilience regulation, including comparative case studies and system-specific considerations
Emerging best practices, incentive challenges, and gaps in current regulatory frameworks
This presentation examines:

## Slide 3
1
2
4
3
Resilience metrics
Industry structures
Resilience in regulation
Agenda
5
Case examples
Key takeaways

## Slide 4
Resilience metrics
Private and Confidential

## Slide 5: Resilience metrics have evolved to encompass a broader set of consequences
Traditional reliability metrics
Outage duration and frequency metrics: SAIDI, SAIFI, MAIFI, CAIDI
Resource adequacy / unserved energy metrics: EUE, ENS, LOLE, LOLH
Restoration and recovery metrics
  Time to recover
  Cost of recovery
  Restoration performance before, during, and after resilience events
Societal and economic consequence metrics
Utility financial impacts
Customer damages and business interruption
Regional economic losses
Social and public health impacts
Capability/robustness metrics
  Asset hardening efforts
  Redundancy and interdependence management
  Response and operational flexibility
  Major storm forecasting and mitigation
Resilience metrics
Sources: U.S. DOE, Grid Modernization: Metrics Analysis (GMLC1.1) – Resilience, World Bank, Measuring the Climate Resilience of the Power Sector: Harmonization, Not Homogenization
Notes: https://gmlc.doe.gov/sites/default/files/2021-08/GMLC1.1_Vol3_Resilience.pdf

## Slide 6
Industry structures
Private and Confidential

## Slide 7: Global industry structures for electric utilities
Industry structures
Global power markets span a continuum from fully integrated monopolies to competitive wholesale and retail markets, with the single-buyer model serving as a common intermediate structure
Vertically Integrated Utility | Single-Buyer Model | Competitive Wholesale Market | Competitive Retail Market
One utility owns generation, transmission, and distribution; prices and investment are approved by government or an independent regulator | Private investors can build generation, but electricity is sold to a national power company or wholesale purchasing agency that has the sole legal right to buy grid-scale electricity, usually through long-term PPAs | Public and private generators, distributors/suppliers, and large end-users participate in the market; prices are market-determined, often through bilateral contracts and/or organized spot markets | Customers can choose their electricity supplier; in some countries only large users have this choice, while in others all consumers do. Retail competition only exists where there is already some form of wholesale competition
Fully integrated utility model, often used where electricity is treated as a natural monopoly | Competition is introduced mainly in generation development, while procurement remains centralized | Competition exists at the wholesale level, with clearer price discovery and investment signals | Competition extends beyond generation into customer-facing supply
Includes state-owned and majority privately owned models | Differences in whether the single buyer owns or does not own generation assets | Competition through bilateral trading with a net or gross pool settlement design | Competition can be partial or full
Bermuda, Guyana, Sudan, Venezuela | Belize, Costa Rica, Honduras, Pakistan, South Africa | Iran, Oman, Uruguay | Australia, China, France, Mexico, United States
Source: Hunt & Shuttleworth, Competition and Choice in Electricity
Notes: https://documents1.worldbank.org/curated/en/099821411252439558/pdf/IDU-b5f7d68f-260d-447c-856b-8660d4282e6e.pdf
https://datacatalog.worldbank.org/search/dataset/0065245/global-power-market-structures-database

## Slide 8: Global power markets have shifted toward competitive structures
Industry structures
Global reform has generally moved utilities from fully integrated monopoly models toward structures that separate monopoly networks from competitive generation and supply, with the single-buyer model often serving as the bridge between the two.
Global power markets have shifted decisively away from vertically integrated monopoly structures. By 2024, these models served only ~7% of the world’s population, versus being the dominant structure in 1989.
Single-buyer models gained traction as a transition model. Their share grew from 8% to 29% of the global population as countries sought to attract private generation investment without fully liberalizing the sector.
Competitive market structures now predominate globally. Organized wholesale and retail competition expanded from under 1% of global population coverage in 1989 to 63% in 2024, reflecting decades of market-oriented sector reform.
Sources: World Bank, Global Evolution of Power Market Designs; World Bank, Rethinking the 1990s Orthodoxy on Power Sector Reform
Competition works well in large power systems but is not always practicable in smaller island economies.

## Slide 9: Shift toward competition changes markets, but the need for reliability and resilience oversight remains the same
1
2
3
4
5
Competition narrows the regulatory focus
Competitive wholesale and retail markets rely on market pricing and investment signals for generation and supply, while regulatory oversight concentrates on transmission and distribution networks, which remain natural monopolies.
Regulation shifts from prices to performance
Reliability and resilience become explicit objectives
Investment oversight adapts to competitive contexts
Hybrid frameworks dominate in practice
As competitive pressures discipline generation and supply, regulators increasingly emphasize service quality, outage performance, system hardening, and restoration outcomes for distribution utilities rather than detailed cost controls alone.
Competitive markets do not inherently deliver resilience; regulators therefore introduce standards, planning requirements, resilience investments, and performance incentives to ensure distribution systems withstand extreme events and recover quickly.
Where generation is market‑driven, regulators must ensure distribution utilities retain clear cost‑recovery pathways for resilience investments, balancing customer affordability with the need for grid hardening and modernization.
Most jurisdictions combine market competition for generation and supply with strong regulatory control of distribution planning, emergency response, and resilience performance, creating layered and hybrid regulatory models.
Industry structures
Sources: World Bank, ESMAP, IEA, NARUC, OECD, GBV
Island power systems’ limited interconnection, smaller scale, and exposure to extreme weather affect reliability and resilience outcomes, requiring context‑sensitive interpretation for comparability with larger, interconnected markets.

## Slide 10
Resilience in regulation
Private and Confidential

## Slide 11: Scope of regulatory oversight of electric utilities
Regulatory structures
Most regions apply layered regulatory frameworks across regional, national, and local levels to balance grid reliability and resilience with market and financial considerations.
 | Standards & Codes | Planning & Adequacy | Investment & Economic Regulation | Operations, Performance, & Assurance
What it is | Standards‑based regulatory regimes define the minimum technical and operational requirements for system reliability and safe operation. | Forward‑looking oversight ensuring the electric system is planned to withstand future stressors, not just today’s load. | Economic regulation that enables, shapes, and constrains resilience investment. | Operational oversight and incentive mechanisms that govern how utilities perform before, during, and after major events.
How it addresses resilience and reliability | Generation & distribution operating & maintenance requirements Interconnection & ride‑through expectations Vegetation management and asset condition standards Mandatory reliability & compliance practices | System planning under extreme weather Load growth, electrification, and DER impacts Resource adequacy, fuel security, and generation diversity Hosting capacity, flexibility, and non‑wires alternatives Stress testing of feeders and substations | Generation winterization Grid hardening Wildfire mitigation & vegetation management Substation upgrades & redundancy Advanced distribution automation & monitoring Backup fuel & black-start capability, on-site resilience tools | Emergency preparedness & storm response Fuel supply and operational readiness for critical resources Restoration speed & customer impacts Mutual aid & logistics readiness Continuous improvement after major events
Regulatory tools | Generator & grid codes Reliability standards Interconnection standards & technical rules Compliance audits & inspections | Distribution system plans or equivalent IRPs and resource adequacy frameworks Resilience and climate vulnerability assessments Scenario and sensitivity analyses (extreme events) | Rate cases & capital plans Resilience riders, trackers, & pre‑approval mechanisms Multi‑year investment allowances Benefit‑cost frameworks for resilience spend | Emergency response & storm plans Restoration performance metrics Performance‑based incentives or penalties Post‑event reports & regulatory reviews
 | Europe / UK, Australia / New Zealand, N. America | US, UK / Europe, Australia | US, Canada, UK / Europe, Australia | US, Canada, Australia / New Zealand, Storm-exposed regions

## Slide 12: Resilience in regulatory oversight
Regulatory structures
Resilience is not addressed through a single rule or metric. It is embedded across technical standards, planning requirements, economic regulation, and utility performance oversight.
Regulatory dimension | How resilience is considered | Examples
Standards & Codes | Resilience is reflected in the minimum technical and operational requirements utilities must meet to maintain safe and reliable service under stressed conditions. | Grid codes, interconnection standards, vegetation management rules, asset condition requirements, reliability standards
Planning & Adequacy | Resilience is incorporated by requiring utilities to plan for future hazards, climate risks, extreme weather, load growth, and evolving system conditions rather than only current reliability needs. | IRPs, distribution system plans, climate vulnerability studies, scenario analysis, stress testing
Investment & Economic Regulation | Resilience is shaped by how regulators approve, fund, and incentivize investments, including whether utilities can recover resilience-related spending and whether the framework favors capex over O&M. | Rate cases, resilience riders, storm protection clauses, multi-year investment plans, totex approaches
Operations, Performance & Assurance | Resilience is measured through how utilities prepare for, respond to, and recover from disruptive events, with oversight focused on service continuity, restoration outcomes, and post-event accountability. | Emergency response plans, restoration metrics, performance incentives, penalties, post-event reviews
Strong resilience regulation spans the full regulatory cycle: setting minimum standards, planning for future risk, enabling investment, and holding utilities accountable for real-world performance.
Notes: https://documents1.worldbank.org/curated/en/099821411252439558/pdf/IDU-b5f7d68f-260d-447c-856b-8660d4282e6e.pdf
https://datacatalog.worldbank.org/search/dataset/0065245/global-power-market-structures-database

## Slide 13: Regulatory tools for addressing resilience
Resilience in regulation
Planning requirements: regulators require utilities to account for hazards and reliability risks in IRPs, transmission plans, or distribution plans, increasingly including climate and disaster scenarios.
Puerto Rico & New York are examples where resilience is embedded through regulator-led planning and vulnerability studies.
Technical and service-quality standards: many countries address resilience through grid codes, continuity standards, outage thresholds, and customer compensation rules.
Chile and Brazil are good examples of standards-driven approaches.
Targeted cost recovery: some jurisdictions explicitly allow utilities to recover resilience investments through riders, clauses, or other tariff mechanisms.
Florida is the clearest example, with a dedicated storm protection cost-recovery clause.
Emergency preparedness and response obligations: resilience is often reflected in rules for weatherization, load shedding, restoration priority, mutual assistance, and post-event review.
Texas is a strong example after Winter Storm Uri – PUC adopted weather emergency preparedness rules
Resource adequacy and reliability payments: in some markets, resilience is incorporated through adequacy mechanisms that value dependable supply during stress events.
Colombia’s reliability charge is one example, designed in part around drought risk.
Governance and statutory objectives: some countries embed resilience directly in electricity law through objectives such as safe, reliable, sustainable service and regulator oversight powers.
Bahamas’s 2024 Electricity Act reforms that codify an independent electricity regulator’s tariff and inspection powers and establish reliability and sustainability objectives
Resilience funding and financing mechanisms: resilience regulation can also address how costs are funded before an event and financed after an event, helping maintain utility financial stability while moderating customer bill impacts.
Ex-ante: California’s wildfire fund shows how jurisdictions can establish funding mechanisms in advance for catastrophic risk.
Ex-post: Florida statute explicitly provides for storm-recovery bonds backed by storm-recovery charges that remain in effect until the bonds are paid in full
Resilience is not typically addressed through a single regulatory tool. Strong frameworks embed it across planning, standards, funding, cost recovery, emergency response, and accountability.

## Slide 14
Case examples
Private and Confidential

## Slide 15: Incentivizing resilience spending
Resilience in utility regulation
Utilities may be reluctant to incur resilience expenditures particularly in the face of political pressure on tariff levels
Affordability concerns and limits on tariff increases can create a disincentive for resilience spending
Underinvestment in traditional regulatory structures
Potential solutions
Totex/Cap-ex Neutrality
Ofgem’s RIIO framework in the UK uses a totex approach that considers capex and opex together
This was conceived to address perceived bias toward capex and is intended to support the most cost-effective resilience solution
Outcome-based Incentives
Links revenue to resilience metrics (i.e., outage frequency/duration, restoration speed)
Example: Australia’s STPIS incentivizes transmission utilities to improve or maintain service performance
Resilience planning obligations
Utilities assess climate risks and incorporate resilience actions into planning and future rate cases (e.g., New York utilities must submit climate vulnerability studies)
Tariff riders that explicitly pass through resilience investment

## Slide 16: Regional case studies and best practices
Resilience in regulation
Case Study | Regulatory Approach | Best Practice
Florida | Utilities must file 10-year storm protection plans covering measures such as overhead hardening, undergrounding, and vegetation management. The framework also provides a separate annual cost-recovery process for prudently incurred storm protection investments. | Pair resilience planning with stable, transparent cost recovery so utilities have both a clear planning mandate and a viable pathway to recover resilience-related investments.
Texas | Following Winter Storm Uri, Texas adopted weatherization and emergency preparedness requirements for critical electric infrastructure, backed by inspections, annual declarations, and enforcement mechanisms. | Translate resilience goals into enforceable standards and compliance requirements rather than relying on voluntary best practices alone.
Puerto Rico | Puerto Rico’s framework ties resilience to a regulator-approved IRP process, supported by resilience-focused system studies and stronger regulatory oversight of utility compliance in a highly disaster-exposed system. | Embed resilience directly into long-term planning and utility decision-making so that it shapes future resource, grid, and investment choices rather than remaining a post-event issue.
Chile | Chile uses technical security and quality-of-service standards that establish minimum operational and service continuity requirements, alongside outage thresholds and customer compensation mechanisms | Use technical codes and service-quality rules to operationalize resilience through clear standards, measurable performance expectations, and accountability to customers.
Columbia | Columbia’s reliability charge is designed to ensure dependable supply during periods of system stress, especially drought-related shortages such as El Niño conditions, by linking resilience to adequacy obligations and market payments. | Incorporate climate and supply risk into adequacy mechanisms and market design so resilience is reflected not only in wires investments, but also in resource sufficiency.
Best practice is not a single resilience metric, but a regulatory framework that links planning, standards, incentives, and accountability to the specific risks utilities face

## Slide 17: How resilience regulation differs across developed, developing, and island power systems
Resilience in regulation
Developed markets
Developing markets
Island nations
More likely to use formal resilience planning, measurable utility performance metrics, and dedicated cost-recovery mechanisms
Greater use of economic regulation to shape resilience investment decisions, including performance incentives and capex-opex neutrality
More institutional capacity for post-event reviews, climate risk integration, and regulatory learning
Illustrative sources: NARUC resilience framework; Ofgem climate resilience reporting
More likely to rely on basic reliability requirements, emergency response protocols, and project-by-project investment approvals
Resilience measures are often constrained by regulatory capacity, utility finances, and access to affordable capital
Greater dependence on public financing, donor support, and concession-backed investment
Illustrative sources: World Bank’s Enhancing Power Sector Resilience report
Similar institutional and financing constraints as developing systems, but greater exposure to extreme weather, fuel dependence, small scale, and limited redundancy
Regulatory focus is often on preparedness, system hardening, rapid restoration, and fuel security
Local financing is often limited, so resilience investments rely on grants, concessional finance, and donor support
Illustrative sources: UNCTAD on building resilience in SIDS and developing states
As systems become smaller, more isolated, and more fiscally constrained, resilience regulation tends to shift from sophisticated performance and planning frameworks toward more practical tools centered on continuity of service, emergency response, and access to external financing.
Notes: IDB: From Risk to Reliability: RESILIENT INFRASTRUCTURE SERVICES TO FACE NATURE'S CHALLENGESEDITED
https://documents1.worldbank.org/curated/en/200771560790885170/pdf/Stronger-Power-Improving-Power-Sector-Resilience-to-Natural-Hazards.pdf
https://docs.wbcsd.org/2014/03/Building_A_Resilient_Power_Sector.pdf

## Slide 18
Key takeaways
Private and Confidential

## Slide 19: Concluding Observations
Key takeaways
Regulators do not address resilience through a single metric or policy. It requires a broad regulatory framework with standards, planning, investment, and operational oversight.
The most effective resilience frameworks link risk identification, utility action, cost recovery, and accountability
Industry structure matters: monopoly systems rely more on direct planning and rate regulation, while competitive systems require stronger market rules and adequacy mechanisms to support resilience
Smaller, developing, and island systems often depend more on practical continuity tools, emergency preparedness, and external financing support than on complex performance-based frameworks
A recurring challenge is facilitating the capital investment and preventive O&M spending required to assure performance and resilience